## Slide 1: TxCRCP-ME Interface Modification Request
11/22/2021
Pangil Choi, P.E.

## Slide 2: STEP 1
DISTRICT
COUNTY
HIGHWAY
PROJECT SCOPE
PROJECT LIMITS
FROM
TO
STA. BEGIN
STA. END
CONTROL
SECTION
JOB
DATE
RM. BEGIN
RM. END
ex) From SH 174 to Hill County Line

## Slide 4: STEP 1/District – Delete
DELETE
Only MAP like County

## Slide 6: Design Traffic – Replace/Use Higher Resolution Image
* Use Form 2124 for traffic data request
: Transportation Planning and Programming Division
Traffic Analysis for Highway Design
Design Traffic
The traffic projections for a highway project (in terms of ADT and one-way total 18-kip ESALs) are obtained from the traffic analysis report provided by the Transportation Planning and Programming Division (TPP). This report is requested during the design phase of a project and, upon receipt, should be evaluated for reasonableness.
Local conditions may cause the directional distribution of heavy vehicles to be unequal. An example is a location near a major quarry adjacent to a highway with otherwise modest levels of truck traffic. If the designer is aware of local conditions that may result in unequal distributions of heavy trucks, TPP should be informed of this condition when requesting traffic projections, and the reported 18-kip ESALS for pavement design should be adjusted.

## Slide 8
zoomable

## Slide 9: Acceptable Punchout per Mile – Replace
Number of Punchouts per Mile
Provide a number of punchouts per mile that is considered the terminal condition of CRCP you are designing. Traditionally, 10 per mile has been the number used for CRCP design. For a higher class of highway where the number of punchouts may be minimized, contact MNT – Pavement Analysis & Design Branch.

## Slide 11: 28-Day Modulus of Rupture – Create Information
28-Day Modulus of Rupture
The Modulus of Rupture (Mr) of concrete is a measure of the flexural strength of the concrete as determined by breaking concrete beam test specimens. Use a 28-day Mr of 570 psi. If the engineer selects an alternate value for Mr, it must be documented with an explanation. Also, if a higher Mr is used, it should be required in the plan to use a higher concrete strength than what is required in Item 360.

## Slide 13: Concrete Elastic Modulus – Create Information
28-Day Modulus of Rupture
Elastic modulus of concrete is an indication of concrete stiffness. It varies depending on the coarse aggregate type used in the concrete. Although the value selected for pavement design could be different from the actual values, the elastic modulus does not have a significant effect on the computed slab thickness. A modulus of 5,000,000 psi should be used for pavement design. The use of a different value must be documented with an explanation.

## Slide 15: Soil Classification System – Delete/Use Higher Resolution Table

## Slide 17: Subgrade Consideration
Popup window & Stay
“Cement Treated Base is highly recommended.”
If a designer selects ML, CL, OL, MH, CH, or OH for soil classification of subgrade, the cement-treated base will be a recommended base type – popup window.

## Slide 19: Subgrade Treatment – Use Higher Resolution Image

## Slide 20
Once engineer selects subgrade type, recommended subgrade treatment guidelines should be popped up.
YES
NO
Cement
Lime-fly ash (FS)
YES
NO
Lime
Lime-cement
Lime-fly ash (FS)
Cement
Fly ash (CS)
Lime
Lime-cement
Lime-fly ash (FS)
Recommended subgrade treatment thickness is greater than 8.0”.
Is the plasticity index <15
Is the plasticity index <35
Recommended
Subgrade Treatment Guidelines
https://ftp.dot.state.tx.us/pub/txdot/mtd/treatment-guidelines.pdf

## Slide 21: Subgrade Treatment Thickness – Use Higher Resolution Image

## Slide 22
Once engineer selects subgrade type, recommended subgrade treatment guidelines should be popped up.
YES
NO
Cement
Lime-fly ash (FS)
YES
NO
Lime
Lime-cement
Lime-fly ash (FS)
Cement
Fly ash (CS)
Lime
Lime-cement
Lime-fly ash (FS)
Recommended subgrade treatment thickness is greater than 8.0”.
Is the plasticity index <15
Is the plasticity index <35
Recommended
Subgrade Treatment Guidelines
https://ftp.dot.state.tx.us/pub/txdot/mtd/treatment-guidelines.pdf

## Slide 25: Base Type – Use Higher Resolution Image

## Slide 26
If the soil types are ML, CL, OL, MH, CH, and OH, a recommended base type should be Cement Treated Base.
Is the plasticity index of subgrade <15
YES
NO
Bond Breaker (≥1.0”) + 6” Cement Treated Base
4” Hot Mix Asphalt Base
Is the soil type
: ML, CL, OL, MH, CH, OH
YES
NO
Bond Breaker (≥1.0”) + Cement Treated Base (≥6.0”)
Bond Breaker (≥1.0”) + Cement Treated Base (≥6.0”)
Hot Mix Asphalt Base (≥4.0”)
Engineer is able to increase the base thickness, but
TxCRCP-ME design input should always be
  No greater than 6” in cement treated base
  No greater than 4” in HMA base
Recommended
Base Type Selection Guidelines

## Slide 28: Print
Font size is too small to be included in the pavement design report.
Default Layout – Landscape with full page

## Slide 30: From email